## Slide 1: MOTEMS
Marine Oil Terminal Engineering and Maintenance Standards
California Seismic Safety Commission
Martin Eskijian, P.E.
Supervisor, Engineering Branch
Marine Facilities Division
California State Lands Commission
March 2005

## Slide 2
MANDATED:
LEMPERT-KEENE-SEASTRAND OIL SPILL PREVENTION AND RESPONSE ACT OF 1990
CURRENT CONDITIONS OF 39 TERMINALS:
Grandfathering – vessel size
Structural degradation
Inadequate fire detection/suppression
Build dates 1901 to 1984 (Average age is 50)
Seismic standards (Were there any?)
MARINE OIL TERMINAL ENGINEERING AND MAINTENANCE STANDARDS (MOTEMS)

## Slide 3
Large Tanker Berthing at an Old, Deteriorated Timber Wharf
Examples of Current Practice
Notes: Large tank vessel, being moored to a very undersized, geriatric timber wharf.

## Slide 4
What Can Happen?
Port of Los Angeles, June 2004

## Slide 5: MOTEMS REGULATORY PROCESS
APPROVAL OBTAINED BY THE STATE LANDS COMMISSION – AUGUST 17, 2004
ADOPTION OBTAINED BY THE CALIFORNIA BUILDING STANDARDS COMMISSION, JANUARY 19, 2005
PUBLISHED - CALIFORNIA BUILDING STANDARDS CODE (TITLE 24, PART 2, VOL 1, CHAPTER 31F)
IN PRINT, APRIL OR MAY 2005, EFFECTIVE 6 MONTHS LATER.
Notes: The cost to rehabilitate was based on one terminal, possible rehab costs could reach $10M, but could be spread out over a number of years. Note that the benefit could be up to $1024 million.

## Slide 6
Audit and Inspection Criteria
Structural Loading Criteria
Seismic Analysis and Design Criteria
Mooring and Berthing Analysis and Design Criteria
Geotechnical Hazards Criteria
Structural Analysis and Design of Components
Piping and Pipeline Criteria
Mechanical, Fire and Electrical Criteria
MOTEMS Scope of the Standards
Notes: Overview of the 11 sections of the MOTEMS.

## Slide 7: MOTEMS SEISMIC/TSUNAMI HAZARD ASSESSMENT
Probabilistic Seismic Hazard Analysis (PSHA) for Southern California Coastal Facilities, J. Savy & W. Foxall, LLNL, 2002.
Tsunami assessment, based on PSHA – performed by Drs. Costas Synolakis and Jose Borrero, University of Southern California
TSUNAMI RUN-UP HEIGHTS (FT):
100 Yr. Return Period 500 Yr. Return Period
Ports of LA and LB 8 ft. 15 ft.
Notes: Based on 41 terminals, this is a preliminary estimate of how many terminals fall into each category. If MOTEMS becomes regulatory in January 2004, the first audits wouldn’t be due until mid 2006.

## Slide 8: MOTEMS SEISMIC/TSUNAMI HAZARD ASSESSMENT
Section 3103F.5.7 of the MOTEMS):
“A tsunami generated by a distant source may allow operators to have an adequate warning for mitigating the risk by departing the marine oil terminal and going into deep water. For near-field events, with sources less than 500 miles away, the vessel may not have adequate time to depart.”
Section 3103F.3.4
“Run-up and current velocity shall be considered in the tsunami assessment…”
Notes: Based on 41 terminals, this is a preliminary estimate of how many terminals fall into each category. If MOTEMS becomes regulatory in January 2004, the first audits wouldn’t be due until mid 2006.

## Slide 9: MOTEMS Seismic Performance Criteria
Performance Criteria:
  Level 1 Earthquake: No or minor structural damage without interruption in service or with minor temporary interruption in service (72 Year Return Period).
  Level 2 Earthquake: Controlled inelastic behavior with repairable damage resulting in temporary closure in service restorable within months. Prevention of major spill. Prevention of collapse (475 Year Return Period).

## Slide 10: SUMATRA EARTHQUAKE/TSUNAMI OF DECEMBER 26, 2004
California Seismic Safety Commission
Martin Eskijian, P.E.
Supervisor, Engineering Branch
Marine Facilities Division
California State Lands Commission
March 2005

## Slide 11: EARTHQUAKE & TSUNAMI INVESTIGATION TEAM INDIA
INVESTIGATE DAMAGE RESULTING FROM THE MAGNITUDE 9 SUMATRA EARTHQUAKE OF DECEMBER 26, 2004
AMERICAN SOCIETY OF CIVIL ENGINEERS
COPRI: SPONSORED (COASTS, OCEANS, PORTS AND RIVERS INSTITUTE)
TCLEE: CO-SPONSORED (TECHNICAL COUNCIL ON LIFELINE EARTHQUAKE ENGINEERING)

## Slide 12: S. India and the Andaman Islands

## Slide 13: ASCE COPRI/TCLEE TEAM SOUTH INDIA - Port of Chennai

## Slide 14: Port of Chennai – 2 Mooring Dolphins Missing

## Slide 15: Container Wharf – Port of Chennai Ebb Current of Tsunami

## Slide 16: Vessel ABG Keshava Impacting Crane (Port of Chennai)

## Slide 17: Crew Leaving Vessel – using Crane as a Gang Way (Port of Chennai)

## Slide 18: Vessel Impacting Wharf

## Slide 19: Vessel Impacting Hoppers on Wharf

## Slide 20: The Shore Temple at Mahabalipuram

## Slide 21: Small fishing/tourist pier (New Construction)

## Slide 22: Small Fishing/tourist pier (post-tsunami)

## Slide 23
PORT BLAIR HARBOUR
ALHW
TIDAL DIFF + 1.0M

## Slide 24: Ferry Terminal Building – Port Blair

## Slide 25: Ferry Terminal Building – Port Blair

## Slide 26: Ferry Terminal Building – Port Blair

## Slide 27: Junglighat Fishing Pier – rubble mount support

## Slide 28: Junglighat Fishing Pier

## Slide 29: Junglighat Fishing Pier

## Slide 30: Junglighat Fishing Pier

## Slide 31: Junglighat Fishing Pier

## Slide 32: Water depth – 1 m more

## Slide 33: Note plastic bags in trees (level of tsunami)

## Slide 34: Tsunami Level almost 2m above floor

## Slide 35: Small vessel pier – tsunami damage

## Slide 36: Port of Port Blair

## Slide 37: Motorcycle parking anyone?

## Slide 38: Left – Pile Supported Wharf Right – backfill area (container wharf)

## Slide 39: Crane Rail – Container Wharf

## Slide 40: New Power/Utilities – Container wharf

## Slide 41: Dry Dock - Port Blair

## Slide 42: Dry Dock – Port Blair

## Slide 43: Barge was on top of wharf

## Slide 44: Pier collapse – Port Blair

## Slide 45
PHOENIX BAY COMPLEX (BEFORE TSUNAMI)
COLLAPSED PORTION
ALHW
FISHERIES JETTY
TIDAL DIFF + 1.0M

## Slide 46
ALHW
COLLAPSED FISHERIES JETTY (AFTER TSUNAMI)
click for video
HIGH MAST LIGHT UNDER COLLAPSE

## Slide 47
PHOENIX BAY COMPLEX (DURING TSUNAMI)

## Slide 48
DAMAGED CAISSON GATE
DAMAGE TO DRYDOCK COMPLEX

## Slide 49: All India Radio – Federal government is providing hand crank transistor radios to neighboring islands

## Slide 50: CONCLUSIONS AND OBSERVATIONS
MOORING LINES WILL “PART” IF SUBJECTED TO 4-5 METERS OF RUN-UP.
RECOMMENDED FAILURE MODE IS “PARTED” LINES, NOT BROKEN OFF BITTS, BOLLARDS OR HOOKS.
TSUNAMI CURRENTS DO NOT GENERALLY “PART” MOORING LINES.
CREWS WILL TRY TO LEAVE THE VESSEL WHEN IN PANIC CONDITIONS.

## Slide 51: CONCLUSIONS AND OBSERVATIONS
LIGHT USE TIMBER WHARVES/PIERS WILL LOSE DECKING OR POSSIBLY COLLAPSE.
CONCRETE/STEEL PILE SUPPORTED MODERN WHARVES/PIERS WILL SURVIVE
TSUNAMI DAMAGE IN A PORT DUE PRIMARILY TO VESSEL IMPACT.
VESSELS UNDER POWER MAY NOT HAVE ENOUGH THRUST TO COUNTER HIGH VELOCITIES ASSOCIATED WITH A TSUNAMI.

## Slide 52: RECOMMENDATIONS
MANDATE UNDERWATER INSPECTION PROGRAM.
PORT PROTOCOL – VESSELS TO LEAVE PORT FOLLOWING AN EARTHQUAKE
ACCELEROMETERS – ON PIERS/WHARVES
A QUICK EGRESS FOR SMALL VILLAGES AND COASTAL AREAS, SIGNS FOR HIGHER GROUND.

## Slide 53: RECOMMENDATIONS
“HARDENED” COMMUNICATION SYSTEM BETWEEN VARIOUS PORTS/COASTAL AREAS.
EMERGENCY COMMUNICATIONS WITH OTHER COUNTRIES, STATES – AREAS CLOSER TO POSSIBLE TSUNAMI.
EDUCATION – MUST BE GENERATIONAL.